## Preventative Maintenance for Drum Fillers

Scale Base:

( : Check accuracy with known weights. (Re-calibration may be required)

( : Overall condition of scale

Lance Assembly:

Visual

( : Inspection of lance carriage rails

( : Inspection of limit switches on lance assembly, check for proper position & tightness

( : Wiper ring

( : Inspect and adjust cam followers

( : Wiper ring

( : Recalibrate lance and ensure encoder is working and counting properly

( : Foot Valve seat and rod packing (check for leaks) …Repack if needed

( : Drip pan

(  : Piping from valve to foot valve (check for leaks)

(  : Foot Valve Actuator

(Required only on Sub-surface Fillers)

(:  Air motor leaks at fittings or valves.

( : Ball Screw (lubricate w/ lithium grease NLGI #2)

Structural:

(: Check for loose bolts and screws

(: Check alignment of chains, sprockets, and gears

(: Check valve actuator mounting and operation of ball valve

(: Check all air lines for leaks at fittings (cylinder, switches, operator enclosure, etc...)

(: Check all air tubing for cracks or abrasion

Filter \Regulator

(: Check for leaks

(: Remove filter and replace if necessary

(: If oiler is attached, check and maintain level w/ (SAE#10 non-detergent oil)

( : *Check operating range during fill cycle.  Required: 70-80 PSI

Enclosures

(: Check Air Lines for leaks "check tubing for cracks or abrasion".

(: Check for moisture or oil in enclosures

(: Visually inspect electronics and connections

(: Check enclosure seals

(: Check all air lines for leaks at fittings (cylinder, switches, operator enclosure, etc...)

Conveyors

(: Condition of rollers and chains

(: Check turn tables and transfer cars for operation

(: Check all gear boxes for fluid and report leaks

(: Check and ensure photo eyes are operational and are aligned

(: Check all alignment guides

CUSTOMER : ______________________________________

DATE:__________________________       INSPECTED BY:_______________________

Note: If necessary, make copies and utilize this sheet. Also please place notes and needed repairs below.